## Slide 1
3DR Pixhawk
Autopilot
3DR uBlox GPS with Compass
Raspberry Pi 2
Model B
Raspberry Pi Camera Board
Ctrl / Data
Ethernet Tether
6600 mAh 4s Lipo Battery
14.8vdc
3DR Power Module
Terminal Board
XT90
XT90
XT60
XT60
GPS
BlueROV Electrical Block Diagram
Terminal Board
+14.8 vdc
Basic 30A ESC
T200 Thruster
ESCs ……6x…..
Basic 30A ESC
T200 Thruster
Thrusters ……6x…..
Pressure Enclosure
Topside (Laptop)
JST-XH
JST-XH
JST-XH
Power 5 vdc
1.2A
……6x…..
Main ESC PWM
Thruster Ctrl
BatPwr In
Power
5 vdc
Buzzer
Buzzer
+14.8 vdc
Mot SW
Safety SW
Not Needed??
What is Best way to Tap into 5v pwr for PI – From Aux Outputs as shown on sht 3?
Gnd
Not Needed??
DRAFT, 20160227
XT60
XT60
+14.8 vdc

## Slide 2
Ref: http://copter.ardupilot.com/wiki/common-pixhawk-overview/
Pixhawk Overview

## Slide 3
Pixhawk connector assignments
ESC - PWM
Pwr Input (from module)
Warning Buzzer ????
Signal from GPS/Compass
Thruster Enable ????
Rasp. PI +5v / - Gnd.
Ref: http://copter.ardupilot.com/wiki/common-pixhawk-overview/

## Slide 4: 3DR Power Module This page explains how to set up the 3DR Power Module (PM) to measure battery voltage and current consumption. The information will also be useful for setting up other types of Power Module.
Ref: http://copter.ardupilot.com/wiki/common-3dr-power-module/
XT60 Connector
To Terminal Board +/Gnd
To Pixhawk Power Input Conn.

## Slide 5: 3DR UBlox GPS + Compass Module This page covers the installation of the 3DR UBlox GPS + Compass module.
Ref: http://copter.ardupilot.com/wiki/common-installing-3dr-ublox-gps-compass-module/