## Slide 1
3DR Pixhawk
Autopilot
3DR uBlox GPS with Compass
Raspberry Pi 2
Model B
Raspberry Pi Camera Board
Ctrl / Data
Ethernet Tether
6600 mAh 4s Lipo Battery
14.8vdc
3DR Power Module
Terminal Board
XT90
XT90
XT60
XT60
GPS
BlueROV Electrical Interconnect Block Diagram
Terminal Board
+14.8 vdc
Basic 30A ESC
T200 Thruster
ESCs ……6x…..
Basic 30A ESC
T200 Thruster
Thrusters ……6x…..
Pressure Enclosure
Topside (Laptop)
JST-XH
JST-XH
JST-XH
Rpi Power 5 vdc
1.2A
Main
Outputs
See Sht. 3
……6x…..
Main ESC PWM
Thruster Ctrl
BatPwr In
Power
5 vdc
Buzzer
Buzzer
(Optional)
+14.8 vdc
Gnd
20160318
XT60
XT60
+14.8 vdc
Connect to aux. output, see Sht. 3 - or can connect to Pixhawk Power Module 5v / Gnd pads see Sht. 5)
GPS
I2C
Compass
I2C Expander
BlueRoboticsPressure / Temp. Sensor
BlueROV-Block-Diagram-20160318.pptx
Sht 1
micro USB
USB
Micro
USB

## Slide 2
Ref: http://copter.ardupilot.com/wiki/common-pixhawk-overview/
Pixhawk Overview
Sht 2
Connect ESCs Control 1-6 Here
Buzzer (Optional)
3DR uBlox GPS
Connect I2C Expander
Then connect uBlox Compass and BlueRobotics Depth Sensor to Expander
Connect 3DR Power Module Pigtail Here
Connect here for Raspberry Pi 5v power
Pi Data connects to Pixhawk via MicroUSB

## Slide 3
Pixhawk connector assignments
Thruster ESCs - PWM
Pwr Input (from module)
Warning Buzzer (optional)
Signal from GPS/Compass
Rasp. PI +5v / - Gnd.
Ref: http://copter.ardupilot.com/wiki/common-pixhawk-overview/
Sht 3
Connect I2c Expander which is connected to uBLOX compass and Bluerobotics depth/temp. sensor
Comms (to Rasp. Pi2)

## Slide 4: 3DR UBlox GPS + Compass Module This page covers the installation of the 3DR UBlox GPS + Compass module.
Ref: http://copter.ardupilot.com/wiki/common-installing-3dr-ublox-gps-compass-module/
Sht 4
I2c Exp
Pressure Sensor
3DR UBlox GPS + Compass

## Slide 5: 3DR Power Module This page explains how to set up the 3DR Power Module (PM) to measure battery voltage and current consumption. The information will also be useful for setting up other types of Power Module.
Ref: http://copter.ardupilot.com/wiki/common-3dr-power-module/
XT60 Connector
To BlueROV
Terminal Board +/Gnd
To Pixhawk Power Input Conn.
Sht 5
3DR Power Module
3DR Power Module-
Reverse Side
+5vdc
Gnd
Connect Pixhawk Power Module 5v / Gnd pads to MicroUSB for Rpi 5v Power

## Slide 6
Comments:
1. The “safety sw” is currently disabled in our recommended
2. I would recommend supplying power to the Raspberry Pi via one of the auxiliary outputs (shown on page 3 of your slides)
3. If you are planning to use a pressure sensor for depth, you will need to use the I2C expander that comes with the PixHawk to connect both the pressure sensor and GPS/compass. (Slide 4)