## Slide 1: BlueROV Electronics and Controls Documentation
Original presentation: https://www.bluerobotics.com/wp-content/uploads/2016/03/BlueROV-Block-Diagram-20160318.pptx
Original forum post: https://www.bluerobotics.com/forums/topic/bluerov-interconnect-diagram/
The AUV Laboratory at MIT Sea Grant
June 24, 2016

## Slide 2
3DR Pixhawk
Autopilot
Raspberry Pi Camera Board
Ctrl / Data
Ethernet Tether
6600 mAh 4s Lipo Battery
14.8vdc
3DR Power Module
Terminal Board
XT90
XT90
XT60
XT60
GPS
BlueROV Electrical Interconnect Block Diagram
Terminal Board
+14.8V DC
Basic 30A ESC
T200 Thruster
ESCs ……6x…..
Basic 30A ESC
T200 Thruster
Thrusters ……6x…..
Pressure Enclosure
Topside (Laptop)
JST-XH
JST-XH
JST-XH
Main
Outputs
……6x….
Main ESC PWM
Thruster Ctrl
BatPwr In
Power
5V DC
Buzzer
Buzzer
(Optional)
+14.8V
Gnd
20160624
XT60
XT60
+14.8V
I2C
I2C Expander
BlueRoboticsPressure / Temp. Sensor
TELEM 2
GPIO15, 14, GND
Raspberry Pi 3
UBEC
Input 14.8V
Output 5V
5V/GND Pins
Xbox Controller

## Slide 3: Controls Interface
QGroundControl
Video Feed
Parameters and Position updates
Sensor Data
Xbox Controller
Manual Control
ArduSub
ESCs
Pi Cam
Raspberry Pi 3
Laptop
Telem2
Sensors
3DR Pixhawk
Autopilot
This is the controls interface for the final ROV setup.
Ethernet
Tether
On-Board
Topside

## Slide 4: Controls Interface- Testing
QGroundControl
Video Feed
Parameters and Position updates
Sensor Data
Xbox Controller
Manual Control
ArduSub
ESCs
Pi Cam
Raspberry Pi 3
Telem2
Sensors
3DR Pixhawk
Autopilot
This is the setup used while testing different components and software packages. Different arrangements could be more compact, but this is what was available and fastest to set up without Ethernet at the time.
Both Mac and PC were used for testing, but unless otherwise noted the interface remained the same between both platforms. An Ubuntu virtual machine on VMware was used for the PC. PuTTY saves time on the PC for SSH without booting the virtual machine.
Ubuntu VM (PC)
Laptop (PC or Mac)
Video Feed (Mac)
SSH (VM)
SSH (Mac or PC)

## Slide 5: Software Summary List of all sites consulted for software downloads, some of the links may be redundant.
https://www.bluerobotics.com/forums/topic/radio-calibration/
http://ardusub.com/initial-setup/#install-qgroundcontrol
https://github.com/mavlink/qgroundcontrol/releases/tag/v2.9.7b
http://firmware.ardusub.com/Sub/latest/
https://www.bluerobotics.com/forums/topic/bluerov-ros-package-updates/
https://www.bluerobotics.com/forums/topic/problem-with-running-bluerov/
http://www.ros.org/install/
Common error fixes
RC3_MAX and RC3_MIN change to 2200 and 800 – fixes joystick/radio calibrating
Change baud rate and a few other parameters listed here http://ardusub.com/initial-setup/#configuring-parameters
ssh into bluerov raspi when simplerov frame is installed on Pixhawk, and UDP com port on qgroundcontrol is 14550: sudo -s mavproxy.py --master=/dev/ttyAMA0 --baudrate 57600 --out LAPTOP_IP_ADDRESS:14550 --aircraft simplerov
If connection times out and mavproxy.py still running: sudo –s pkill mavproxy.py

## Slide 6
http://copter.ardupilot.com/wiki/common-pixhawk-overview/
Pixhawk Overview
Connect ESCs Control 1-6 Here
Buzzer (Optional)
Connect I2C Expander
Then connect Pressure Sensor and BlueRobotics Depth Sensor to Expander
Connect 3DR Power Module Pigtail Here
Pi Data connects to Pixhawk via Telem 2

## Slide 7
Pixhawk connector assignments
Thruster ESCs - PWM
Pwr Input (from module)
Warning Buzzer (optional)
http://copter.ardupilot.com/wiki/common-pixhawk-overview/
Connect I2c Expander which is connected to Pressure sensor and Bluerobotics depth/temp. sensor
Comms (to Rasp. Pi3)

## Slide 8: Raspberry Pi Connectors The pins are labeled in a confusing manner, so this page is to clarify the connections necessary to run the Pixhawk and Raspberry Pi together.
http://tr1.cbsistatic.com/hub/i/2016/03/03/53945d8c-6ec9-4a2a-922a-6df3b2a5c372/img4085.jpg, http://ardupilot.org/dev/_images/RaspberryPi_Pixhawk_wiring1.jpg
UBEC 5V
UBEC GND
Telem2 #3
Telem2 #2
Telem2 #6

## Slide 9: 3DR Power Module This page explains how to set up the 3DR Power Module (PM) to measure battery voltage and current consumption. The information will also be useful for setting up other types of Power Module.
http://copter.ardupilot.com/wiki/common-3dr-power-module/
XT60 Connector
To BlueROV
Terminal Board +/Gnd
To Pixhawk Power Input Conn.
3DR Power Module
3DR Power Module-
Reverse Side
+5vdc
Gnd

## Slide 10: UBEC This page explains how to set up the 3A-6s UBEC Voltage regulator to power Raspberry Pi from LiPo safely.
http://www.brontoseno.com/kategori-produk/sbecubec/
To BlueROV
Terminal Board +/-
Turnigy UBEC-5A
Input
To Raspberry Pi 5V and Gnd pins
Output

## Slide 11: ESC Connections
http://docs.bluerobotics.com/assets/images/documentation/besc-labels.png
5V not needed, cut the connections to avoid overheating
Motor directions determined by output phase, exact wiring not known until tested

## Slide 12: OPTION - Bluerobotics Lumen Light(s)
***Lights Setup
The lights feature is currently setup to support lights that use a standard servo PWM signal for control. Until light support is officially added to QGC, the “Gimbal Roll” settings are used to connect the light input to a servo output.
Select an available channel for the “Output channel” and RC9 for the “Input channel”.
http://ardusub.com/initial-setup/#lights-setup
Connect the Signal wire and Ground to Aux Output on Pixhawk ***
(Appropriate microcontroller pin for Brightness Control)
  Yellow: PWM (3-48 volts)
  Provide a servo PWM pulse from 1100 μs (off) to 1900 μs (brightest)
Connect the power wires to power Terminal Board
  Red: +10-48 volts
  Black: Ground
  Yellow: PWM (3-48 volts)
Lumen
Light
  Black: Ground
  Red: +10-48 volts
Lumen
Light
  Additional Lights can be connected in Daisy Chain Fashion
PIX
Aux
https://www.bluerobotics.com/store/electronics/lumen-light-r1/

## Slide 13: OPTION - Use of an Ethernet Breakout to allow removal / replacement of penetrator from endcap without cutting wires.

## Slide 14: OPTIONAL - Adaptor for USB Connection Between Pixhawk and Pi
Crius RGB External LED Indicator USB Module for Pixhawk Flight Controller
http://www.amazon.com/Crius-External-Indicator-Pixhawk-Controller/dp/B00LAV9VLM?ie=UTF8&psc=1&redirect=true&ref_=oh_aui_detailpage_o01_s00
We found that direct USB connectionfrom Rasberry Pi to Micro USB connector on side of 3DR Pixhawk was unreliable so we used the following interface circuit to make the connection

## Slide 15: Penetrators
Original Configuration
Main (4”) Enclosure (10 Holes)
Vent/Purge
Thruster 1
Thruster 2
Thruster 3
Thruster 4
Thruster 5
Thruster 6
Tether
Pressure/Temp
LED Light
No Spares
All Penetrators locations are interchangeable
Note: 14-hole Endcap is Available from Blue Robotics
End Cap with 10 Holes (4″ Series)
Aluminum End Cap with 14 Holes (4″ Series)

## Slide 16
Comments:
The “safety sw” is currently disabled in our recommended
Changes have been made to diagram to power Raspberry Pi separately from Pixhawk
ESC 5V connections removed by rec.
GPS/Compass removed because ocean water
Slides 1, 3, 4, 5, 8, 10, 11 added for clarity

## Slide 17: Additional Sources
https://www.bluerobotics.com/wp-content/uploads/2016/06/Diagram-Mockup-Ethernet.jpg
https://www.bluerobotics.com/forums/
http://ardupilot.org/dev/docs/raspberry-pi-via-mavlink.html
http://ardusub.com/initial-setup/#configuring-parameters
https://www.bluerobotics.com/forums/topic/radio-calibration/

## Slide 18: Additional Images

## Slide 19: Additional Images